## Slide 1
AXON
Bearing fault
diagnosis at the edge
A real-data demo using the Paderborn Bearing DataCenter
TensorFlow-ready workflow, deployed with a validated Random Forest reference model
64 kHz
vibration
17 Oct 2026
Notes: Open the dashboard at http://127.0.0.1:8501/. Introduce AXON as an edge-native bearing diagnosis system. Source: official Paderborn Bearing DataCenter website.

## Slide 2
Demo objective
Show that AXON accepts a vibration window, runs local inference, and returns a traceable diagnostic record.
The question
Can a locally deployed model distinguish a healthy bearing from a bearing with documented damage?
What the demo proves
• Real Paderborn vibration data
• Checksum-verified model bundle
• API and MQTT edge inference paths
• Diagnostic record with evidence and confidence
Scope: healthy vs documented bearing damage. Location-specific claims require more pure fault bearings.
AXON bearing demo | 2
Notes: Be explicit about scope before showing accuracy. The selected KIs include mixed inner and outer damage, so the deployed classifier returns documented bearing damage instead of an unsupported location label.

## Slide 3
Real-world data and label evidence
Only official bearing fact sheets supplied labels. Raw data remains local and is not committed to GitHub.
3
physical healthy bearings
6
physical damaged bearings
108
recordings retained
13,448
vibration windows
Sampling and preparation
64 kHz vibration channel • 4,096 samples per window • 50% overlap • 3 recordings per bearing and operating condition
The storage cap keeps the local demo reproducible without creating synthetic samples or mixing one physical bearing across evaluation partitions.
AXON bearing demo | 3
Notes: Source: Paderborn Bearing DataCenter official fact sheets K001, K002, K003, KA04, KA15, KA16, KI04, KI14, and KI16. The dataset is CC BY-NC 4.0. Each fact sheet determines whether the bearing is healthy or has documented damage.

## Slide 4
Inference pipeline
The same feature contract runs in training, the API, and the edge process.
1
Vibration window
4,096 samples at 64 kHz
→
2
Feature extraction
16 time and frequency features
→
3
Random Forest
200 trees, balanced classes
→
4
Diagnostic record
class, confidence, evidence
Input contract check: exact sample count and sampling frequency required. Invalid inputs return SENSOR_DATA_INVALID rather than a prediction.
AXON bearing demo | 4
Notes: The 16 features include mean, standard deviation, RMS, variance, peak measures, crest factor, skewness, kurtosis, energy, dominant frequency, spectral centroid, entropy, and band energy. Demonstrate that inference rejects incompatible signal shape or frequency.

## Slide 5
Held-out physical-bearing validation
The model never saw K003 or KI04 during training.
95.3%
balanced accuracy
95.3%
macro F1
2,981
held-out windows
Held-out confusion matrix
Predicted healthy
Predicted damage
True healthy
True damage
1,493
0
140
1,348
Train: K001, KA04, KA15, KA16, KI16 Validation: K002, KI14 Test: K003, KI04
AXON bearing demo | 5
Notes: Metrics apply only to this prepared Paderborn subset and to windows from the held-out physical bearings. Do not generalize the metric to other motors, sensors, or operating regimes without validation.

## Slide 6
Live demonstration
Use the local dashboard and API to show one healthy result and one documented-damage result.
1
Open dashboard
http://127.0.0.1:8501/
2
Show model status
AXON Bearing RF v1, 64 kHz, 4,096 samples
3
Submit healthy vibration
Expected: HEALTHY_WITHIN_VALIDATED_SCOPE
4
Submit damaged vibration
Expected: FAULT_SUSPECTED with technician confirmation
Close with the limitation: results support a technician’s inspection decision; they do not replace it.
Notes: Demo URL: http://127.0.0.1:8501/. The verified live API response showed a healthy real Paderborn window with 1.0 uncalibrated confidence. The edge inference code also returned FAULT_SUSPECTED for a documented-damage Paderborn window. Keep the technical caution visible in spoken delivery.